ANNEXES

ANNEX 1

ALLOCATION OF LABEL ELEMENTS

annex 1

### ALLOCATION OF LABEL ELEMENTS

For the GHS, the assigned pictogram, signal word and hazard statement are given in that order for each hazard category of the hazard class. Where the hazard class and or categories are covered under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the assigned corresponding pictogram is given for each category below the GHS requirements.

| EXPLOSIVES |
| --- |
| Unstable explosives | Division 1.1 | Division 1.2 | Division 1.3 | Division 1.4 | Division 1.5 | Division 1.6 |
|  |  |  |  |  | No pictogram 1.5 on orange background | No pictogram 1.6 on orange background |
| Danger Unstable explosive | Danger Explosive; mass explosion hazard | Danger Explosive; severe projection hazard | Danger Explosive; fire, blast or projection hazard | Warning Fire or projection hazard | Danger May mass explode in fire | No signal word No hazard statement |
| No pictogram assigned in the UN Model Regulations (Transport not allowed) |  |  |  |  |  |  |
| Notes on the colours of the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram elements: For Divisions 1.1, 1.2 and 1.3: Symbol exploding bomb: black; background: orange; Division number (1.1, 1.2 or 1.3, as appropriate) and compatibility group (*) in bottom half and figure “1” in bottom corner: black. (2) For Divisions 1.4, 1.5, 1.6: Background: orange; Figures: black; Compatibility group (*) in bottom half and figure “1” in bottom corner: black. (3) The pictogram for Divisions 1.1, 1.2 and 1.3 is also assigned to substances which have an explosive subsidiary risk, but without the indication of the division number and the compatibility group (see also “Self-reactive substances” and “Organic peroxides”). |

| Flammable gasES |
| --- |
| Category 1 | Category 2 | - | - | Note |
|  | No pictogram |  |  | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the symbol, number and border line may be shown in black instead of white. The background colour stays red in both cases. |
| Danger Extremely flammable gas | Warning Flammable gas |  |  |  |
|  | Not required under the UN Model Regulations |  |  |  |

| FLAMMABLE AEROSOLS |
| --- |
| Category 1 | Category 2 | - | - | Note |
|  |  |  |  | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the symbol, number and border line may be shown in black instead of white. The background colour stays red in both cases. |
| Danger Extremely flammable aerosol | Warning Flammable aerosol |  |  |  |

| OXIDIZING GASES |
| --- |
| Category 1 | - | - | - | Note |
| Danger May cause or intensify fire; oxidizer |  |  |  |  |
|  |  |  |  | Pictogram colours: Symbol and number: black. Background: yellow. |

| GASES UNDER PRESSURE |
| --- |
| Compressed gas | Liquefied gas | Refrigerated liquefied gas | Dissolved gas | Note |
|  |  |  |  | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram elements: (1) Not required for toxic or flammable gases. (2) The symbol, number and border line may be shown in white instead of black. The background stays green in both cases. |
| Warning Contains gas under pressure; may explode if heated | Warning Contains gas under pressure; may explode if heated | Warning Contains refrigerated gas; may cause cryogenic burns or injury | Warning Contains gas under pressure; may explode if heated |  |

| FLAMMABLE LIQUIDS |
| --- |
| Category 1 | Category 2 | Category 3 | Category 4 | Note |
|  |  |  | No pictogram | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the symbol, number and border line may be shown in black instead of white. The background colour stays red in both cases. |
| Danger Extremely flammable liquid and vapour | Danger Highly flammable liquid and vapour | Warning Flammable liquid and vapour | Warning Combustible liquid |  |
|  |  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods Model Regulations |  |

| FLAMMABLE SOLIDS |
| --- |
| Category 1 | Category 2 | - | - | Note |
|  |  |  |  | Colours for pictogram under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations: Symbol and figure: black. Background: white with seven vertical red stripes. |
| Danger Flammable solid | Warning Flammable solid |  |  |  |

| SELF-REACTIVE SUBSTANCES AND MIXTURES |
| --- |
| Type A | Type B | Types C and D | Types E and F | Type G |
|  |  |  |  | There are no label elements allocated to this hazard category |
| Danger Heating may cause an explosion | Danger Heating may cause a fire or explosion | Danger Heating may cause a fire | Warning Heating may cause a fire |  |
| Same as for explosives (follow same symbol selection process) |  |  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations |
| Notes: (1) For Type B, under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, special provision 181 may apply (Exemption of explosive label with competent authority approval. See Chapter 3.3 of UN Model Regulations for more details). (2) UN Model Regulations pictogram colours: - Self-reactive substance pictogram: Symbol and figure: black. Background: white with seven vertical red stripes. - Explosives pictogram: Symbol (exploding bomb): black; background orange; figure “1” in the bottom corner: black. |

| PYROPHORIC LIQUIDS |
| --- |
| Category 1 | - | - | - | Note |
|  |  |  |  | Colours of UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram: Symbol and figure: black. Background: upper half: white; lower half: red. |
| Danger Catches fire spontaneously if exposed to air |  |  |  |  |

| PYROPHORIC SOLIDS |
| --- |
| Category 1 | - | - | - | Note |
|  |  |  |  | Colours of UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram: Symbol and figure: black. Background: upper half: white; lower half: red. |
| Danger Catches fire spontaneously if exposed to air |  |  |  |  |

| SELF-HEATING SUBSTANCES AND MIXTURES |
| --- |
| Category 1 | Category 2 | - | - | Note |
|  |  |  |  | Colours of UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram: Symbol and figure: black. Background: upper half: white; lower half: red. |
| Danger Self-heating; may catch fire | Warning Self-heating in large quantities; may catch fire |  |  |  |

| SUBSTANCES AND MIXTURES, WHICH IN CONTACT WITH WATER, EMIT FLAMMABLE GASES |
| --- |
| Category 1 | Category 2 | Category 3 | - | Note |
|  |  |  |  | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the symbol, number and border line may be shown in black instead of white. The background stays blue in both cases. |
| Danger In contact with water releases flammable gases which may ignite spontaneously | Danger In contact with water releases flammable gases | Warning In contact with water releases flammable gases |  |  |

| OXIDIZING LIQUIDS |
| --- |
| Category 1 | Category 2 | Category 3 | - | Note |
|  |  |  |  | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram colours: Symbol and number: black. Background: yellow. |
| Danger May cause fire or explosion; strong oxidizer | Danger May intensify fire; oxidizer | Warning May intensify fire; oxidizer |  |  |
| OXIDIZING SOLIDS |
| Category 1 | Category 2 | Category 3 | - | Note |
|  |  |  |  | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram colours: Symbol and number: black. Background: yellow. |
| Danger May cause fire or explosion; strong oxidizer | Danger May intensify fire; oxidizer | Warning May intensify fire; oxidizer |  |  |

| ORGANIC PEROXIDES |
| --- |
| Type A | Type B | Types C and D | Types E and F | Type G |
|  |  |  |  | There are no label elements allocated to this hazard category |
| Danger Heating may cause an explosion | Danger Heating may cause a fire or explosion | Danger Heating may cause a fire | Warning Heating may cause a fire |  |
| Same as for explosives (follow same symbol selection process) |  |  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |
| Notes: (1) For Type B, under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, special provision 181 may apply (Exemption of explosive label with competent authority approval. See Chapter 3.3 of UN Model Regulations for more details). (2) UN Model Regulations pictogram colours: - Organic peroxide pictogram: Symbol (flame): black or white; background: upper half: red; lower half: yellow; Figure “5.2” in the bottom corner: black. - Explosives pictogram: Symbol (exploding bomb): black; background orange; figure “1” in the bottom corner: black. (3) The label conforming to the colouring scheme in the table for oxidizing liquids may be used until 1 January 2011. |

| CORROSIVE TO METALS |
| --- |
| Category 1 | - | - | - | Note |
|  |  |  |  | Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, pictogram colours: Symbol: black background: upper half: white; lower half: black with white border; Figure 8: white. |
| Warning May be corrosive to metals |  |  |  |  |

| ACUTE TOXICITY: ORAL |
| --- |
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 |
|  |  |  |  | No pictogram |
| Danger Fatal if swallowed | Danger Fatal if swallowed | Danger Toxic if swallowed | Warning Harmful if swallowed | Warning May be harmful if swallowed |
|  |  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods , Model Regulations. Note: For gases under the UN Model Regulations , replace the number 6 in the bottom corner of the pictogram by 2. UN Model Regulations pictogram colours: Symbol and figure: black. Background: white. |

| ACUTE TOXICITY: SKIN |
| --- |
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 |
|  |  |  |  | No pictogram |
| Danger Fatal in contact with skin | Danger Fatal in contact with skin | Danger Toxic in contact with skin | Warning Harmful in Contact with skin | Warning May be harmful in contact with skin |
|  |  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. Note: For gases under the UN Model Regulations, replace the number 6 in the bottom corner of the pictogram by 2. For UN Model Regulations pictogram colours: Symbol and figure: black. Background: white. |

| ACUTE TOXICITY: INHALATION |
| --- |
| Category 1 | Category 2 | Category 3 | Category 4 | Category 5 |
|  |  |  |  | No pictogram |
| Danger Fatal if inhaled | Danger Fatal if inhaled | Danger Toxic if inhaled | Warning Harmful if inhaled | Warning May be harmful if inhaled |
|  |  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. Note: For gases under the UN Model Regulations, replace the number 6 in the bottom corner of the pictogram by 2. For UN Model Regulations pictogram colours: Symbol and figure: black. Background: white. |

| SKIN CORROSION/IRRITATION |
| --- |
| Category 1A | Category 1B | Category 1C | Category 2 | Category 3 |
|  |  |  |  | No pictogram |
| Danger Causes severe skin burns and eye damage | Danger Causes severe skin burns and eye damage | Danger Causes severe skin burns and eye damage | Warning Causes skin irritation | Warning Causes mild skin irritation |
|  |  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. Note: UN Model Regulations pictogram colours: Symbol: black background: upper half: white; lower half: black with white border; Figure 8: white. |

| SERIOUS EYE DAMAGE/ EYE IRRITATION |
| --- |
| Category 1 | Category 2A | Category 2B | - | - |
|  |  | No pictogram |  |  |
| Danger Causes serious eye damage | Warning Causes serious eye irritation | Warning Causes eye irritation |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

(

| Respiratory SENSITIZATION * |
| --- |
| Category 1 | - | - | - | - |
| Danger May cause allergy or asthma symptoms or breathing difficulties if inhaled |  |  |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

| SKIN SENSITIZATION(* |
| --- |
| Category 1 | - | - | - | - |
| Warning May cause an allergic skin reaction |  |  |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

| Germ cell mutagenicity |
| --- |
| Category 1A | Category 1B | Category 2 | - | - |
| Danger May cause genetic defects (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Danger May cause genetic defects (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Warning Suspected of causing genetic defects (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

| CARCINOGENICITY |
| --- |
| Category 1A | Category 1B | Category 2 | - | - |
| Danger May cause cancer (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard ) | Danger May cause cancer (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard ) | Warning Suspected of causing cancer (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard ) |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |
| TOXIC TO REPRODUCTION |
| Category 1A | Category 1B | Category 2 | Additional Category on effects on or via lactation | - |
|  |  |  | No pictogram |  |
| Danger | Danger | Warning | No signal word |  |
| May damage fertility or the unborn child (state specific effect if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard ) | May damage fertility or the unborn child (state specific effect if known)(state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard ) | Suspected of damaging fertility or the unborn child (state specific effect if known)(state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard ) | May cause harm to breast-fed children. |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

| SPECIFIC TARGET ORGAN SYSTEMIC TOXICITY (SINGLE EXPOSURE) |
| --- |
| Category 1 | Category 2 | Category 3 | - | - |
| Danger Causes damage to organs (or state all organs affected, if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Warning May cause damage to organs (or state all organs affected, if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Warning (respiratory tract irritation) May cause respiratory irritation or (Narcotic effects) May cause drowsiness and dizziness |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

| SPECIFIC TARGET ORGAN SYSTEMIC TOXICITY (REPEATED EXPOSURE) |
| --- |
| Category 1 | Category 2 | - | - | - |
| Danger Causes damage to organs (state all organs affected, if known) through prolonged or repeated exposure (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Warning May cause damage to organs (state all organs affected, if known) through prolonged or repeated exposure (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) |  |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

| ASPIRATION HAZARD |
| --- |
| Category 1 | Category 2 | - | - | - |
| Danger May be fatal if swallowed and enters airways | Warning May be harmful if swallowed and enters airways |  |  |  |
| Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations. |

| AQUATIC TOXICITY (ACUTE) |
| --- |
| Category 1 | Category 2 | Category 3 | - | Note |
|  | No pictogram | No pictogram |  | For Category 1, under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the pictogram is not required if the substance presents any other hazards covered by UN Model Regulations. If no other hazard is presented (i.e. for UN Nos. 3077 and 3082 in Class 9 of the UN Model Regulations), this pictogram is required as a mark in addition to the UN Model Regulations Class 9 label. |
| Warning Very toxic to aquatic life | No signal word Toxic to aquatic life | No signal word Harmful to aquatic life |  |  |
|  | Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations |  |  |

| AQUATIC TOXICITY (CHRONIC) |
| --- |
| Category 1 | Category 2 | Category 3 | Category 4 | Note |
|  |  | No pictogram | No pictogram | For Categories 1 and 2, under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the pictogram is not required if the substance presents any other hazards covered by UN Model Regulations. If no other hazard is presented (i.e. for UN Nos. 3077 and 3082 in Class 9 of the UN Model Regulations), this pictogram is required as a mark in addition to the UN Model Regulations Class 9 label. |
| Warning Very toxic to aquatic life with long lasting effects | No signal word Toxic to aquatic life with long lasting effects | No signal word Harmful to aquatic life with long lasting effects | No signal word May cause long lasting harmful effects to aquatic life |  |
|  |  | Not required under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations |  |

# Footnotes

( 	Further work is included in the work programme of the Sub-Committee of Experts on the GHS.

( 	Further work is included in the work programme of the Sub-Committee of Experts on the GHS.

# Text boxes

1.1

1.2

1.3